## MPU6050 test tool for raspberry Pi
### Background information
https://invensense.tdk.com/wp-content/uploads/2015/02/MPU-6000-Datasheet1.pdf
https://invensense.tdk.com/wp-content/uploads/2015/02/MPU-6000-Register-Map1.pdf
https://github.com/Blokkendoos/mpu-calibration

### Preparations
Enable I2C:	sudo raspi-config > Interface Options > I2C > Yes
Install i2cdetect:	sudo apt-get install i2c-tools
Connect MPU and check wiring.

Check if MPU6050 is available:	i2cdetect -y 1 > should be appear at address 0x68
### IMU_test

This is a test tool to check and learn something about the Motion Processing Unit MPU6050.
One can read all register and save the settings to a CSV file just as test.

It's also possible to cyclic read the Accelerometer, Temperature and Gyroscope values.
You will also see the current scale setting for Accelerometer and Gyroscope in Info column.
The same can be seen in a rolling chart.

For testing and settings it is possible to write into a register or overwrite all write-able with zero.

Some options, settings and special actions are on the Tools/Settings page too.
Some terminal commands – good to know:
Read a byte from MPU:	i2cget -y 1 0x68 0x75 (Who am I, it's own address)
Read a word from MPU:	i2cget -y 1 0x68 65 w (result comes as big endian)
Write a byte to MPU register:	i2cset y 1 0x68 107 0 (wake-up command)
Read temperature cyclic (raw):	watch -n 0.5 'i2cget -y 1 0x68 65 w'

## Programming contactless potentiometer AS5600
### AS5600 Register

Read Register with button "AS5600 Reg". Same as button Read CONF but jumps to Table to see all register values for verification.
To read values from data registers click on "AS5600 Cyc" (Read cyclic).

Note: To change Conf register do not change n/a bits. Those may contain factory settings.
Programming (Option A with I²C)

Use the correct hardware configuration (Option A and C).

Option A: Write CONF register
Option C: Set Maximum Angle

Burn: Permanently save both.

### Usage

Connect AS5600 to Raspberry Pi with I²C interface and power up the AS5600.
Start the tool "IMU_test". Go to Page "AS5600". It will go to "AS5600" page if this is the only detected sensor on I²C bus.

Read the register of AS5600.
Button "AS5600 Reg" or button "Read CONF"
### Calibration procedure

Step 1: Turn the magnet to the start position.
Step 2: Read the RAW ANGLE register. Write the RAW ANGLE value into the ZPOS register. Wait at least 1 ms.
Button "2. Set Zero Pos"
Step 3: Rotate the magnet in the direction defined by the level on the DIR pin (GND for clockwise, VDD for counterclockwise) to the stop position. The amount of rotation must be greater than 18 degrees.
Step 4: Read the RAW ANGLE register. Write the RAW ANGLE value into the MPOS register. Wait at least 1 ms. Proceed with Step 6 to permanently program the configuration.
Button "4. Set Max Pos"

Step 5: Perform a BURN_ANGLE command to permanently program the device. Wait at least 1 ms.
Button 5. Burn A
Step 6: Verify the BURN_ANGLE command: Write the commands 0x01, 0x11 and 0x10 sequentially into the register 0xFF to load the actual OTP content. Read the ZPOS and MPOS registers to verify that the BURN_ANGLE command was successful.
Button "6. Read OTP"

Step 7: Read and verify the ZPOS and MPOS registers again after a new power-up cycle.
Button "AS5600 Reg"

Note:	Do not touch Configuration, at least do not burn config.
Basically, do only something when you exactly know what you are doing,
especially "Burn" actions.
Before perform a burn-command read carefully the rules and restictions
for the OTP mentioned in AS5600 datasheet.

### HW settings

Sensor connected to Raspberry Pi by I²C interface.

I²C bus SCL and SDA is 3.3V signal.
PGO pin is not needed when programming via I²C.

Power supply is 3.3V. It canbe done by camera or Raspberry PI.
GND must be connected to Raspberry Pi.